## Slide 1: STM-GARSOS processing
From GAR-SOS radial data to STM spatial coefficients
Concise overview of the historical stable workflow

## Slide 2: Objective and model
Represent each dynamic image as X_t(x,y)=\sum_{\ell=1}^{L} {\rm ST}_{t,\ell}(x,y) C_\ell(x,y).
Estimate L spatial coefficient images from multicoil radial data.
Synthesize the complete dynamic image series after the coefficient solve.

## Slide 3: Raw-data preparation
Load GAR-SOS metadata, raw k-space, and a vendor-reconstructed reference volume.
Correct readout delay and prepare partition data.
Estimate/apply coil-noise whitening.
Generate normalized [kx, ky, kz] trajectory coordinates.
Compute radial density-compensation weights.

## Slide 4: Frame formation
Flattened arrays retain one row per readout/partition/spoke sample.
Spokes are grouped consecutively into temporal frames.
Historical baseline: 15 spokes per frame and approximately 133 complete frames.
Incomplete trailing spokes are discarded.

## Slide 5: Calibration-data path
Each frame is reconstructed with 3-D Kaiser-Bessel gridding.
Oversampled grid: approximately 308 x 308 x 132.
3-D inverse FFT and centered resize produce a 224 x 224 x 96 volume.
A selected z slice is transformed to 2-D Cartesian k-space.
A central 32 x 32 calibration square is extracted.

## Slide 6: STM calibration
k_{\rm Cal} is supplied to \texttt{STM\_computation}.
The calibration data span the temporal frames.
The STM algorithm estimates ST maps and eigenvalues.
Historical baseline: L = 7 and 224 x 224 spatial map dimensions.

## Slide 7: Radial STM data
The historical baseline used a direct centered 58-point partition IFFT.
One z index is selected and the coil dimension is preserved.
Output radial data: [readout x spokes/frame x coils x frames].
In-plane kx/ky coordinates are retained for the NUFFT.

## Slide 8: Multicoil radial operator
Forward: d_c={\cal N}_{\rm radial}(S_c \odot X).
Adjoint: {\cal F}^H(d)=\sum_c S_c^* \odot {\cal N}_{\rm radial}^H(d_c).
Sensitivity maps are forward receive-coil maps.
Coils remain separate in the data fidelity term.

## Slide 9: STM operator and PCG
STM synthesis maps coefficients C to dynamic images X.
The radial operator maps X to predicted multicoil radial data.
Solve ({\cal A}^H{\cal A})C={\cal A}^H y with PCG.
Optional Tikhonov solve adds lambda I.

## Slide 10: Output and historical caveats
Output: coefficient images plus synthesized [224 x 224 x frames] image series.
The initial baseline used the direct 58-point z/partition IFFT.
Later work addresses forward-map estimation, z-grid consistency, scaling, and conditioning.
The slides describe the original stable path, not all later corrections.