## Slide 1: STM-GARSOS processing
Detailed methods presentation
Historical stable workflow through spatial-coefficient estimation

## Slide 2: Reconstruction objective
Dynamic image model: X_t(x,y)=\sum_{\ell=1}^{L}{\rm ST}_{t,\ell}(x,y)C_\ell(x,y).
Unknown: C_l(x,y), an [Nx x Ny x L] coefficient volume.
Measured data: multicoil radial samples for each temporal frame.
Goal: fit the measured radial data while restricting temporal variation to the STM subspace.

## Slide 3: Entry point and inputs
main_STM_GARSOS loads input k-space identifiers and scan metadata.
A vendor-reconstructed reference volume defines target geometry.
prepareGARSOSSTMData creates shared prepared data and calibration metadata.
Historical defaults: 15 spokes/frame, 32 x 32 calibration square, L = 7.

## Slide 4: Prepared trajectory and data
sampledData: [nReadout x nPartitions x nSpokes, nCoils].
kSpaceLocations: flattened [kx, ky, kz] rows.
spokeIndex: one identifier per flattened sample.
DCF: one radial density-compensation value per sample.
Coordinates use normalized cycles/FOV-like units.

## Slide 5: Trajectory construction
k_x=\rho\cos(\phi) and k_y=\rho\sin(\phi).
rho is the centered readout coordinate normalized by readout length.
phi follows the GAR-SOS spoke-angle convention.
kz is generated from the partition index and acquisition geometry.
The arrays are flattened in readout/partition/spoke order.

## Slide 6: Readout processing and whitening
Readout delay correction is estimated from selected calibration lines.
Readout Fourier processing is applied before the final flattening.
Partition padding is performed during preparation.
Noise covariance is estimated from noise acquisitions.
The whitening transform is applied across receive channels.

## Slide 7: Density compensation
The existing DCF is based on radial shell-sector area.
It is generated from the in-plane radius and readout increment.
Frame-specific DCF values are selected with the frame samples.
Calibration gridding applies DCF and additional reconstruction weights.
The later STM radial operator uses its prepared radial samples and NUFFT convention.

## Slide 8: Frame grouping
Unique spoke identifiers define the acquisition order.
nFrames = floor(nSpokes / nSpokesPerFrame).
Each frame contains all readout and partition samples for its spokes.
Incomplete trailing spokes are excluded.
For the baseline, 15 spokes/frame produced approximately 133 frames.

## Slide 9: Calibration reconstruction
reconstructGARFrameForSTM selects frameData, frameTrajectory, and frameDCF.
Coordinate transform and translation phase correction are applied.
Gaussian/spatial weighting and DCF scaling are applied.
GpuReconstructur20181008 grids every coil separately.
The class applies inverse FFT, resize/deapodization, and coil-profile accumulation.

## Slide 10: 3-D grid and target geometry
Target image geometry: imageSize = [224, 224, 96].
Oversampled grid: gridSize = ceil(1.375 x imageSize) = [308, 308, 132].
Samples are deposited with a 3-D Kaiser-Bessel kernel.
ifftn is applied on the oversampled Cartesian grid.
shiftAndResize maps the result to the centered 224 x 224 x 96 grid.

## Slide 11: Calibration k-space extraction
Select reconstructedVolume(:, :, zSlice).
Apply fftshift(fft2(ifftshift(senseImage))).
Extract the centered calibration square with localCentralRegion.
Baseline calibrationSize = [32, 32].
Single-slice kCal has dimensions [32 x 32 x nFrames].

## Slide 12: STM computation
\texttt{STM\_computation} receives k_{\rm Cal}, desired map dimensions, L, and options.
The calibration data encode temporal correlations across frames.
The algorithm estimates ST_maps [Nx x Ny x Nt x L].
eigenValues provide a diagnostic of model rank/content.
The baseline used L = 7 because more modes appeared informative than in the Cartesian demo.

## Slide 13: Historical z-slice preparation
prepareGARSOSSliceDataForMCNUFFT restores [readout, partition, spoke, coil].
It applies the selected translation phase and coordinate transform.
Historical baseline: centered direct IFFT along the 58 partition entries.
The requested zIndex is selected from that 58-point result.
This differs from the later 58-to-96 gridded z-only correction.

## Slide 14: Radial STM data dimensions
After frame grouping: radialData [nReadout x nSpokesPerFrame x nCoil x nFrame].
kxy [nReadout x nSpokesPerFrame x nFrame].
The in-plane radial trajectory is retained.
The coil dimension is not combined before the STM solve.
Trajectory/data correspondence is validated before operator construction.

## Slide 15: Forward sensitivity-map model
Forward coil model: d_c={\cal N}_{\rm radial}(S_c\odot X).
S_c are forward receive sensitivities in the whitened channel basis.
Adjoint coil combination is \sum_c S_c^* d_c after NUFFT adjoints.
This is distinct from calibration-only coil-combination profiles.
Map and dynamic-data channel ordering must match.

## Slide 16: Radial NUFFT operator
buildGARSOSRadialEncodingOperator creates one NUFFT plan per frame.
Forward: multiply by coil maps, then NUFFT each coil.
Adjoint: NUFFT-adjoint each coil, then sum conjugated maps.
Optional single precision converts trajectories, maps, data, and outputs.
The operator exposes forward, adjoint, and vectorized forms.

## Slide 17: STM operator composition
buildGARSOSSTMOperators composes STM synthesis with radial encoding.
\mathcal{A}(C)=\mathcal{F}(\mathcal{S}(C)).
\mathcal{A}^H(y)=\mathcal{S}^H(\mathcal{F}^H(y)).
The normal operator is applied without explicitly forming a matrix.
The coefficient vector has Nx x Ny x L entries.

## Slide 18: PCG solve
Right-hand side: b=\mathcal{A}^H y.
Unregularized system: (\mathcal{A}^H\mathcal{A})C=b.
The baseline used tolerance 1e-5 and up to 50 iterations.
Residual history, status flag, iteration count, and elapsed time are stored.
Preconditioning and Toeplitz support were preliminary rather than baseline assumptions.

## Slide 19: Optional Tikhonov solve
Regularized system: (\mathcal{A}^H\mathcal{A}+\lambda I)C=b.
The implementation can run a second PCG solve with lambda.
The effective lambda depends on data, map, NUFFT, and DCF scaling.
A numerical lambda should not be compared across differently scaled operators without calibration.

## Slide 20: Synthesis and outputs
\widehat{X}_t=\sum_{\ell=1}^{L}{\rm ST}_{t,\ell}\widehat{C}_\ell.
sense_recon_stm has dimensions [Nx x Ny x nFrame].
The result also contains coefficient images and PCG diagnostics.
The initial reported output contained approximately 133 reconstructed frames.

## Slide 21: Baseline versus later improvements
Baseline: direct 58-point partition IFFT for STM slice data.
Later work: forward sensitivity-map estimator and map-semantics audit.
Later work: coil-preserving gridded z-only path for the 96-slice geometry.
Later work: scaling, conditioning, coverage, regularization, and preconditioning analysis.
These improvements should be presented separately from the historical baseline.

## Slide 22: End-to-end summary
Raw GAR-SOS data -> corrected, whitened radial samples.
Trajectory + DCF + spoke IDs -> temporal frames.
3-D gridding -> calibration Cartesian k-space -> central square.
STM calibration -> ST maps and eigenvalues.
Coil-resolved radial data + sensitivity maps -> STM/radial operator.
PCG -> spatial coefficients -> dynamic image series.